## Slide 1: IACV Project F08 sıngle vıew 8 ball pool wıth contınuıty correctıon
By: Mustafa Çağatay Sipahioğlu
10899801 - 220591

## Slide 2
Taking a single view video of an 8 Ball Pool Game
  Detect & Classify the Balls
  Find the Game State
Problem Statement

## Slide 3
This is simply a object detection and classification problem: ML Models
  Near perfect performance when done right
  Requires too much processing
  Hard to develop
State of the Art

## Slide 4
Use a simple, deterministic detection & classification model.
Tune some parameters
Focus on the ball tracking aspect to improve continuous performance of the model.
Our Approach

## Slide 5
A video is simply a set of consequent frames. To analyse the video we must first get these frames.
We have first created a sampling code to sample a frame every sampling_period seconds from the video.
  Lower period -> More samples -> Better Ball Tracking BUT Longer Runtime
  Sample a frame every 0.1 seconds. (The default for a 30fps video is 0.033 s.)
We will work on the image of the table. We have the option to enlarge or contract the image before processing it.
  More enlarged image -> More pixels between the ball images -> Contour detection works better BUT More Computational Load
  Take the width of the rectified table as 1440px. (About 2x enlargement)
Performance Variables

## Slide 6
Class: Cue (C) , 8 Ball (8) , Solid (O) , Striped (||)
State: Positional sector on the table --->
  Inside octant: State= 21-28
  Next to hole: State= 11-16
Center: of the smallest enclosing circle.
Contour: Pixel array defining the perimeter.
Image: Image of only the ball on the table.
Luminance: Average LAB luminance of pixels.
Color Ratio: Colored Pixels / Whiteish Pixels
Define a Ball

## Slide 7
Class: Cue (C) , 8 Ball (8) , Solid (O) , Striped (||)
State: Positional sector on the table
  Inside octant: State= 21-28
  Next to hole: State= 11-16
Center: of the smallest enclosing circle.
Contour: Pixel array defining the perimeter.
Image: Image of only the ball on the table. --->
Luminance: Average LAB luminance of pixels.
Color Ratio: Colored Pixels / Whiteish Pixels
Define a Ball

## Slide 8: Chapter 1: Detecting and Classifying Balls

## Slide 9
Step 1: Extract and Rectify the Table
Focus only on the workspace
Make the balls have similar dimensions
Detection & Classification

## Slide 10
Step 2: Remove the Table Cloth
Use a color range mask to eliminate green tones
Focus only on the balls
Make contour detection much easier
Detection & Classification

## Slide 11
Step 3: Detect Contours
Contour is the physical space the ball occupies
Calculate physical parameters from the contour
  Radius ( of the enclosing circle)
  Center ( of the enclosing circle)
  Aspect Ratio ( of the enclosing rectangle)
  Area
Filter the ball-like contours:
  Radius in tuning range
  Aspect ratio – Square-ish
  Area in tuning range
Detection & Classification

## Slide 12
Step 4: Classify the Ball-Like Contours
Luminance Classification
  Hole < 8 Ball < Solid < Striped < Cue
  Delete ‘Hole’ class contours.
  Best for classifying Hole, 8 Ball, Cue
The lighting near the top of the table is brighter than near the bottom of the table.
Striped and Solid Balls can have similar Lumini.
Color Ratio Classification
  Cue < Striped < Solid < 8 Ball
  Best for differentiating Solid, Striped Balls
Detection & Classification

## Slide 13
Step 5: Check Classification Feasibility
Multiple ‘C’ detected:
  Only the highest luminance is ‘C’ rest are ‘||’
Multiple ‘8’ detected:
  Only the lowest luminance is ‘8’ rest are ‘O’
Impossible extra ‘O’ detected:
  Look at the low color ratio ‘O’s.
  The highest luminance one should be a ‘||’
Impossible extra ‘||’ detected:
  Look at the high color ratio ‘||’s.
  The lowest luminance one should be a ‘O’
Detection & Classification

## Slide 14: Chapter 2: Continuity of Stationary Balls

## Slide 15
Motive: Be able to detect very close balls as 2 separate balls.
Method: Remember balls that are stationary, detect new balls from the changing part of the image between frames.
Continuity of Stationary Balls

## Slide 16
Step 1:
Check Which Balls in the Before Frame Didn’t Move
Continuity of Stationary Balls

## Slide 17
Step 2:
Remove the Stationary Balls from the new image.
Continuity of Stationary Balls

## Slide 18
Step 3:
Detect the balls.
(Now we will detect only the moved balls)
Continuity of Stationary Balls

## Slide 19
Step 4:
Combine the stationary balls and the detected moved balls to detect all the balls in the frame.
(Including the balls that are left behind other balls: see the purple solid ball behind the 8 Ball)
Continuity of Stationary Balls

## Slide 20: Chapter 3: Continuity of Moving Balls

## Slide 21
Step 1: Master Balls
Master Ball = De Facto Numbered Ball
Update the Master Balls using the new frame.
Try matching master balls to the balls in new frame.
Continuity of Moving Balls

## Slide 22
Step 2: Match Stationary Balls to Masters
If the saved image of a master ball didn’t change, this ball didn’t move.
Match it to itself.
Continuity of Moving Balls

## Slide 23
Step 3: Find the Moved Balls
Remove the stationary balls from the new frame.
Now, Detected balls = Moved Balls.
Continuity of Moving Balls

## Slide 24
Step 4: Match the Slightly Moved Balls
If a moved ball’s center is still in the contour of a master ball: match this moved ball to that master ball.
Continuity of Moving Balls

## Slide 25
Step 5: Match the Noticeably Moved Balls
If there are multiple moved and matched balls that need matching:
Calculate the distance between each moved-master ball combination. Match them starting from the closest.
Continuity of Moving Balls

## Slide 26
Step 6: If Moved Balls Still Need Matching:
These must belong to some master balls that were not detected before. (Populate the master balls with the excess moved balls)
Also works as a correction mechanism for master balls mistakenly classified to be potted.
Continuity of Moving Balls

## Slide 27
Step 7: If Master Balls Still Need Matching:
There are not enough balls on the table. These master balls were either potted (If they were near a hole sectors 1_) or they are set to be undetected.
We will look for these master balls again in the next frames and correct our verdict if we are mistaken.
Continuity of Moving Balls

## Slide 28
Step 9: Make Sure the Cue Ball is Detected
The classification of the cue ball works great and it is almost guaranteed to always be on the table. We check our master balls in case a cue ball was matched to the wrong master ball. (Happens due to stationary continuity if it strikes a ball very fast and stops in the striked ball’s former position)
Continuity of Moving Balls

## Slide 29
Achieved results:
Extract, rectify, mask (remove table cloth) of an 8 Ball Pool Table.
Detect contours, filter ball-like contours.
Deterministically classify balls. (Depending on luminance and or color ratio of a ball)
Differentiate and track each of the 16 balls separately, in the following cases:
  A ball stayed stationary.
  A ball moved only slightly.
  A ball moved noticeably.
  A ball was potted.
Do self-correction for classes of a ball when a ball becomes undetected-detected again.
Conclusion

## Slide 30
Better image pre-processing: Improve classifier performance.
Better contour detection: Correctly detect balls during breaking or in fast shots involving multiple close-by balls.
Better ball classification: If we had a very reliable classifier we wouldn’t have to implement this good of a ball tracking algorithm to make sure we classify balls correctly.
Ball classification history: We do not implement class correction to a continuously tracked ball. So it is imperative for us to have detected that ball correctly in the beginning or we would have to hope that we will get to redetect it to reclassify it.
A mechanism where the mode of the detected class history is checked every once in a while for classification corrections could be implemented.
Future Work

## Slide 31
Find the visual center of a concave contour: Pole of inaccessibility problem, needed in case the centroid of a concave contour ends up inside a convex contour.
Future Work

## Slide 32
This project takes an 8 Ball Pool game video shot in a stationary single-view And it demonstrates how a simple tuned deterministic vision model can be used to keep track of the game state using the continuity between frames and game logic.
Final Result

## Slide 33: Q&A